## Slide 1
access link options:
1x400 GE
2x200 GE
4x100 GE
Optical signals options:
1x OTSi@400G
2x OTSi@200G split into 2x MCs
2xOTSi@200G into 1x MC
4x OTSi@100G split into 4x MCs (*)
3x OTSi@100G split into 2x MCs (2+1 OTSis)
2xOTSi@100G split into 2x MCs
4x OTSi@100G into 1x MC
mapping options:
1xODUflex@400G->ODUC4/OTUC4
2xODUflex@200G->ODUC4/OTUC4
2xODUflex@200G->2xODUC2/OTUC2
4xODUflex@100G->ODUC4/OTUC4
4xODUflex@100G->2xODUC2/OTUC2
4xODUflex@100G->4xODUC1/OTUC1
4xODU4/OTU4
This is the only option which can be implemented using standard G.698.2 application codes
It is worth noting that it could be possible to put 4xOTSiG@100G using G.698.2 application codes (with 50GHz channel spacing) into one MC@200GHz. Since this configuration does not provide spectrum optimization, it is considered as a special configuration of using 4x adjacent MCs@50GHz
OT
digital
optical
OTU | OTSi
Eth | ODU

## Slide 2
Notes:
From an optical perspective, these two OT configurations are indistinguishable:
2x200GE->2xODUflex@200G->ODU4C/OTU4C->2xOTSi@200G->2xMCs
2x200GE->2xODUflex@200G->2xODU2C/OTU2C->2xOTSi@200G->2xMCs
However, from management/control perspective, the lifecycles and routes of the 2x OTSis/MCs shall be the same in the former case, while they can be different in the latter case
If the 2xMCs are adjacent, the two OT configurations are also indistinguishable from this configuration:
2x200GE->2xODUflex@200G->ODU4C/OTU4C->2xOTSi@200G->1xMC
The case where only one 200GE/ODUflex/ODUC2/OTUC2 is configured, can be seen as partial configuration of both (complete) configurations:
2x200GE->2xODUflex@200G->2xODU2C/OTU2C->2xOTSi@200G->2xMCs
With only 1x200GE->1xODUflex@200G->1xODU2C/OTU2C->1xOTSi@200G->1xMC active
1x200GE+2x100GE->1xODUflex@200G+2xODUflex@100G->1xOTSi@200G+2xOTSi@100G->3xMCs
With only 1x200GE->1xODUflex@200G->1xODU2C/OTU2C->1xOTSi@200G->1xMC active

## Slide 3
Router
OT1
OT2
OT3
OT4
1xOTUC4/400G-ZR->4xOTSi@100G(G.698.2)->4xMCs (to be co-routed)
OLS-0
Is this correct?
400G-ZR has only one OTSi@400G
100 GE
100 GE
100 GE
100 GE
access link options:
4x100 GE
Optical signals options:
4x OTSi@100G split into 4x MCs (*)
mapping options:
4xODUflex@100G->4xODUC1/OTUC1